## Slide 1: Mercury: Detecting the Performance Impact of Network Upgrades
Ajay Mahimkar, Han Hee Song* , Zihui Ge, Aman Shaikh,
Jia Wang, Jennifer Yates, Yin Zhang* , Joanne Emmons
AT&T Labs – Research * UT-Austin
ACM SIGCOMM 2010, New Delhi, India

## Slide 2: Increasing Network Complexity
Massive scale
100s of offices, 1000s of routers,
10,000s of interfaces,
Millions of consumers
Immense software complexity
Scale, Bugs, Interactions
Diverse technologies and vendors
Layer-1, Layer-2, Switches, Routers,
IP, Multicast, MPLS, wireless access points
Continuous evolution
Upgrades, Installations
Applications
Scale, sensitivity

## Slide 3: What are Network Upgrades?
  Fundamental changes to the network
  Router software or hardware upgrades
  Configuration and policy changes
Upgrades can result in unpredictable impacts in performance
  Impacts might fly under radar
Enterprise
System
Servers
Operator
packet loss
End Users
  Goals
  Introduce new service features
  Reduce operational cost
  Improve performance
Notes:   Expected changes: e.g., software upgrades lead to improvement in router CPU utilization
  Unexpected changes: e.g., performance degradation caused by bugs in the new release of software

## Slide 4: Monitoring Impact of Upgrades
One aspect: extensive lab testing before deployment
  Software engineering principles and certification process
  Goal is to prevent bugs from reaching the network
Problems with lab testing
  Cannot replicate scale and complexity of operational networks
  Cannot enumerate all test-cases
Important to monitor upgrades in-field
  Manual investigation: critical issues are caught after a long time
  Operations Challenge: Large number of devices and performance event-series
Innovative solutions required to monitor at scale

## Slide 5: Mercury
Detects the performance impact of upgrades in operational networks
  Automated data mining to extract trends
  Scalable across a large number of measurements
  Flexible to work across a diverse set of data sources
  Ease of interpretation to network operations
Challenges
  How to extract upgrades?
  Do upgrades induce behavior changes in performance?
  Is there commonality in configuration across devices?
  Is the change observed network-wide?

## Slide 6: Extracting upgrades
Minimize dependency on domain expert input
  Human information can be unreliable, incomplete, or outdated
  Our approach is data-driven: mine configuration & workflow logs
Operating system upgrades
  Track OS version and upgrades using polling
Firmware upgrades
  Detect difference in hardware configuration across days
Upgrade-related configuration changes
Lots of configuration changes
    Frequent changes like provisioning customers are not upgrades
  Heuristic: look for “out of the ordinary”
    Two metrics: high coverage (skewness) and rareness

## Slide 7: Detecting Upgrade Induced Changes
Performance event-series creation
Divide each series into equal time-bins
For example, daily counts or averages
Behavior change detection
E.g., a persistent level-shift
Changes in means, medians, standard deviations or distributions
Our Approach:
  Recursive Rank-based Cumulative Sums (CUSUM)
  Outputs significant changes along with magnitude (positive versus negative)
Upgrades
U1
U2
Associating changes to upgrades
Proximity Model: Same location and close in time
CUSUM Si = Si-1 + (ri – ŕ)
S0 = 0

## Slide 8: Identifying commonality
Extracting common attributes helps drill-down into changes
Software configuration
  Example attributes are OS version, number of BGP peers, re-routing policies
Device location, role, model, vendor
Problem: Identifying common attributes is a search in a multi-dimensional space
Classical machine learning problem
Solution: RIPPER rule learner
Outputs rules of form A => B
E.g., if (upgrade = OS change) and (router role = border)
=> positive level-shift in CPU
Change
A1
Attributes
A2
An
+
-
+
Upgrade
. .
.
.
An-1

## Slide 9: Detecting Network-wide Changes
Why network-wide change detection?
  Changes might be missed for rare events at each device
  Aggregation across devices increases the change significance
  How to aggregate event-series for each upgrade type?
  For each event-series, identify devices that are upgraded
  Not trivial to simply aggregate - each upgrade applied over several days
  Solution: Time alignment for each upgrade
  Align event-series such that upgrade falls on same date
Significant Change
after aggregation
Upgrade date
Upgrade date
R1
R2
R3

## Slide 10: MERCURY Evaluation
Evaluation using real network data is challenging
  Lack of ground truth information
  Close interaction with network operations
Data Sets
  Upgrades: router configuration, workflow logs
  Performance event-series: SNMP (CPU, memory) and syslogs
  Collected from tier-1 ISP backbone over 6 months
  Number of routers = 988
  Router categories: core, aggregate, access, route reflector, hub
Notes: Our approach: Close interaction with operators
  Validation using operators’ domain knowledge
  Experience using case studies

## Slide 11: Extracting Upgrades
Upgrade Labels from Operations | Counts | MERCURY Labels | Counts
Interesting | 13 | False negative | 1
Non-interesting | 19 | False positive | 11
MERCURY Output
Filtered after applying behavior change detection
r = 2
r = 4
r = 10
r = 6
r = 8
Compare Mercury output with labels from operations
  False positive: falsely detected by Mercury
  False negative: missed by Mercury
  Vary the threshold for detecting rare upgrade-related configuration changes
r = 4

## Slide 12
Performance Event-series | Count | Upgrades | Upgrade Event-series Pairs | Upgrade induced change-points | Unique Cases
CPU | 988 | 185 | 182,780 | 338 | 10
Memory | 988 | 185 | 182,780 | 160 | 4
Syslogs | 288,084 | 185 | 53,295,540 | 3181 | 92
MERCURY Output
Significant reduction
MERCURY not only confirmed earlier findings,
but also revealed previously unknown network behaviors
Upgrade induced Behavior Changes
Router Role | Core Routers | Aggregate Routers | Access Routers | Route Reflectors | Hub Routers | Total
Performance series | 103,112 | 43,226 | 113,079 | 6,548 | 24,095 | 290,060

## Slide 13: Mercury Findings Summary
Operating system upgrades
  Downticks in CPU utilizations on access routers
  Upticks in memory utilizations on aggregate routers
  Varying behaviors in layer-1 link flaps across different OS versions on access routers
  Upticks in number of protection switching events on access routers
Firmware upgrades
  Downticks in CPU utilizations on central CPU and customer-facing
  Upticks on optical carrier line cards
BGP fast external fall-over policy changes
  Upticks in the number of “down interface flaps”
  Downticks in the number of BGP hold timer and peer closed session events

## Slide 14: Case Study: Protection Switching
Line card protection in access routers
To protect customers from line card failures
On failure, customers are switched to backup
  Switching is called Automated Protection Switching (APS)
OS upgrade
Dates normalized across all upgraded routers. The upgrade happened on day 84
MERCURY validated a known issue
Small increase in the frequency of APS failure events
  Critical issue impacting customers
Run across all the syslog messages
  APS failure events are rare per router
  Statistically indistinguishable on an individual router level
  Change detected when aggregated across all upgraded access routers
Mercury was used by Ops to track improvements as fix was deployed

## Slide 15: Conclusions
Mercury detects persistent changes in performance induced by upgrades
  Automated detection with minimal domain knowledge
  Scalable to a large number of measurements
  Flexible to be applied across diverse data sources
Operational Experiences
  Confirmed earlier findings as well as discovered previously unknown behaviors
  Is becoming a powerful tool inside AT&T
Future Work – Lots !!!
  Apply Mercury to new domains such as data centers, VoIP, IPTV, Mobility
  Behavior changes induced by chronic events
  Real-time capabilities

## Slide 16
Thank You !