## Slide 1
CQRD: A Switch-based Approach to Flow
Interference in Data Center Networks
Guo Chen
Dan Pei, Youjian Zhao
Tsinghua University, Beijing, China
Notes: Hello everyone, this is Guo Chen. I’m currently a PHd student in Tsinghua University. My research interests include flow scheduling, load balance and fault-tolerance in in data center networks. Today I’m going to talk about CQRD: A Switch-based Approach to Flow Interference in Data Center Networks. This is a jointwork with Dan Pei and Youjian Zhao.

## Slide 2: The Problem
Flow interference dramatically
increases the flow completion time (FCT)
of short delay-sensitive flows in data center networks (DCN)
Notes: Today, many real-time interactive services such as web search or retail are deployed in data centers. These services generate a lot of short delay-sensitive flows which contribute the majority of flows in data center networks.
However, flow interference dramatically increases the flow completion time of these short delay-sensitive flows in DCNs.

## Slide 3: Flow Interference
Short delay-sensitive flows (majority in DCN) have to wait a long time at switches for buffer and bandwidth resources occupied by a few of long bandwidth-greedy flows (e.g., backup, replication)
Notes: Flow interference describes the phenomenon that short delay-sensitive flows have to wait a long time at switches for buffer and bandwidth resources occupied by
a few of long bandwidth-greedy flows.
This may cause packet loss of short flows, and dramatically increases their flow completion time.

## Slide 4: Flow Interference
Short delay-sensitive flows (majority in DCN) have to wait a long time at switches for buffer and bandwidth resources occupied by a few of long bandwidth-greedy flows (e.g., backup, replication)
Caused by coarse Output Queue (OQ) switch queue management scheme
Notes: Essentially, flow interference is caused by the coarse Output Queue (OQ) queue management scheme used in today’s DCN switches.
As a result, short flows have to contend for the same buffer and bandwidth resources with long flows, which greatly affects the performance.

## Slide 5: Prior solutions
Transport Layer Rate Control:
  DCTCP [SIGCOMM’10]
  HULL [NSDI’12]
  D2TCP [SIGCOMM’12]
  D3 [SIGCOMM’11]
Preemptive Flow Scheduling:
  PDQ [SIGCOMM’12]
  pFabric [SIGCOMM’13]
Modification to end host and/or switch hardware
New protocol stack and switch hardware
Notes: Many prior works including transport layer solutions and preemptive flow scheduling architectures try to get around the coarse queue management problem by optimizing flows’ rate assignment and scheduling to keep the switch queues near empty.
However, all these approaches need to modify end host’s protocol stack and face deployment hurdles.

## Slide 6: Intuition of CQRD
Tackling the root cause of flow interference:
Need a more fine-grained queue management scheme
Notes: Different from these previous approaches, we address the DCN flow interference problem by directly tackling its root cause, which is the coarse switch queue management scheme.
We argue that the flow interference calls for a more fine-grained queue management scheme than the current output queue scheme in the commodity DCN switches.

## Slide 7: The Goal
Goal:
  Alleviate flow interference
  Reduce FCT of short delay-sensitive flows
  Maintain high goodput of long bandwidth-greedy flows
Objectives:
  Transparent to end host
  No modification to protocol stack
  Based on underlying techniques available in commodity productions
Notes:   With this intuition, our goal is to alleviate flow interference. We aim to reduce FCT of short delay-sensitive flows, while maintaining high goodput of long bandwidth-greedy flows.
  Our solution must be readily deployed in current DCN environments. Thus, it should be transparent to end host and with no modification to protocol stack. Also, it should be based on underlying techniques available in commodity productions.

## Slide 8: Our Solution
CQRD:
A fine-grained switch queue management scheme to flow interference
Notes: As such, we propose a simple and cost-effective queue management scheme, CQRD, to address the flow interference problem in DCNs.
The proposed approach only requires a minor revision to the switches’ queue management scheme, without any coordination among switches, and without any modification to end hosts.

## Slide 9
Agenda
Background & Motivation
Flow Interference
CQRD Design
Evaluation
Conclusion
Notes: Before introducing our CQRD solution, we use a toy example to show how flow interference impairs the performance, because of the coarse OQ switch queue management scheme.

## Slide 10: Toy Example: Flow Interference in OQ Switch
NS2 simulation parameters:
  Link capacity=10Gbps, Link delay=4us, Total buffer size=288KB, TCP initial window size=4, TCP initial RTO=200us.
8x8 switch connected to host 1-8, Host 1-5 sending 10KB TCP flow to host 8, Host 6-7 sending 100MB TCP flow to host 8
Notes: We use NS2 to simulate an 8 port OQ DCN switch, with each port connected to an end host. All the simulation parameters are listed below. At time 0, both servers 6 and 7 start to send a 100MB TCP flow to server 8. Five milliseconds later, servers 1-5 start 5 delay-sensitive tasks and each sends a 10KB TCP flow to server 8.

## Slide 11: Toy Example: Flow Interference in OQ Switch
FCT
Goodput
Short flows completed in ~100ms
Goodput of short flows collapse
Notes: Now, we look at each flow’s FCT and goodput.
The 5 short flows have been completed in ~100ms. However, they should have been completed in less than 100us without interference.
Also, their goodput collapse.

## Slide 12: Toy Example: Flow Interference in OQ Switch
FCT
Goodput
Short flows completed in ~100ms
Goodput of short flows collapse
Interfered
by these 2 long flows
Notes: This is because the short flows are interfered by this 2 long flows in OQ switch. During this situation, the output queue of port 8 is quickly filled up with packets of flow 6 and 7. Thus, packets of flow 1-5 are continuously dropped when they reach the switch. As a result, their flow completion time soar up to hundreds of milliseconds.

## Slide 13: Toy Example: Flow Interference in OQ Switch
FCT
Goodput
Short flows completed in ~100ms
Goodput of short flows collapse
Interfered
by these 2 long flows
Unfairly served
Notes: What’s more, these two long flows are interfered by each other and unfairly served as well, due to the coarse queue management scheme.
From this we can see that flow interference could greatly impair the performance of DCN.

## Slide 14
Agenda
Background & Motivation
Flow Interference
CQRD Design
Evaluation
Conclusion
Notes: Apparently, flow interference calls for a more fine-grained switch queue management scheme. Next, we introduce the design of our CQRD approach.

## Slide 15: CQRD Design
Crosspoint-Queue
Notes: The design of CQRD is very simple, but fine-grained enough to achieve desirable flow separation to avoid interference from each other. The basic idea of CQRD is two-fold:
First, CQRD allocates separate crosspoint queue with the same capacity for each pair of inputs and outputs.

## Slide 16: CQRD Design
Crosspoint-Queue
  Eliminating interference between flows on different switch paths
  (Output-Contending but not Path-Contending, OC-PC)
Notes: Arriving packets are first stored in the crosspoint buffer and wait to be scheduled out by the output scheduler. CQRD uses Round-Robin scheduling for each output to schedule the packets. It ensures that each XB is fairly served.
This eliminates interference between flows on different switch paths.

## Slide 17: CQRD Design
Crosspoint-Queue
  Eliminating interference between flows on different switch paths
  (Output-Contending but not Path-Contending, OC-PC)
Separate buffer
&
Fair scheduling
Notes: Thus, Separate buffers and fair scheduling provides separation for those flows which are Output-Contending but not Path-Contending. On the contrary, these flows have to contend for the same output buffer in traditional OQ switches.

## Slide 18: CQRD Design
Crosspoint-Queue
  Eliminating interference between flows on different switch paths
  (Output-Contending but not Path-Contending, OC-PC)
Random-Drop
  Alleviate the flow interference within the same switch path (Path-Contending, PC)
Notes: Second, CQRD use random-drop scheme to alleviate the flow interference within the same switch path (which is also called Path-Contending, PC). When the corresponding crosspoint queue is full, CQRD takes random-drop scheme upon packet arrival.

## Slide 19: CQRD Design
Crosspoint-Queue
  Eliminating interference between flows on different switch paths
  (Output-Contending but not Path-Contending, OC-PC)
Random-Drop
  Alleviate the flow interference within the same switch path (Path-Contending, PC)
Occupy more buffer,
more likely to be dropped
Notes: A flow’s packets will be more likely to be dropped if this flow occupies most of the buffer, and vice versa. As such, if several small flows are contending for the same buffer with a large flow, packets of those small flows still have a reasonable chance to get into the buffer even if the buffer are currently filled up by the large flows.

## Slide 20: CQRD Design
Crosspoint-Queue
  Eliminating interference between flows on different switch paths
  (Output-Contending but not Path-Contending, OC-PC)
Random-Drop
  Alleviate the flow interference within the same switch path (Path-Contending, PC)
Occupy more buffer,
more likely to be dropped
Notes: Based on these two simple and mature underlying techniques, which are crosspoint-queue and random-drop, CQRD provides a fine-grained queue management scheme, and greatly alleviate the flow interference problem.

## Slide 21: Toy Example: Flow Interference
FCT
Goodput
3 orders shorter FCT
3 orders higher goodput
Notes: We also do the same experiment in CQRD as the toy example before, using the same total amount of 288KB buffer as OQ switch.
As we can see, with CQRD, the FCT of delay-sensitive flows can be 3 orders of magnitude lower than the OQ switch. Also, the goodput of those flows are 3 orders of magnitude higher. CQRD utilizes the separated buffers to eliminate the flow interference of flows between different switch paths, which greatly improve the performance as shown in this toy example.

## Slide 22: Toy Example: Flow Interference
FCT
Goodput
3 orders shorter FCT
3 orders higher goodput
Fairly served
Almost no cost of
goodput
Notes: Meanwhile, CQRD switch achieves a very good fairness among flows.
Although buffers are separated according to the input and output port pair, and can’t exploit statistical multiplexing as OQ, the capacity of separated buffers is still large enough for long flows to maintain high goodput in CQRD as in OQ switch. As we can see in the figure, the two large flows almost has the same goodput as in OQ switches.

## Slide 23: Toy Example: Flow Interference
FCT
Goodput
3 orders shorter FCT
3 orders higher goodput
Fairly served
Almost no cost of
goodput
Notes: The former toy example only shows CQRD’s ability of improving performance under a single and simple situation. No flows contend for the same switch path.

## Slide 24
Agenda
Background & Motivation
Flow Interference
CQRD Design
Evaluation
Conclusion
Notes: Next, we evaluate the performance of CQRD using thorough simulations in NS2 under more realistic and complicated conditions. We compare CQRD’s performance with two other switch-based approaches, the original OQ and the state-of-art HCF approach.

## Slide 25: Evaluation
1. How much FCT of short delay-sensitive flows is reduced in CQRD?
2. How much goodput of long bandwidth-greedy flows is sacrificed in CQRD?
Notes: In the evaluation, we try to answer the following two questions.
1. How much FCT of short delay-sensitive flows is reduced in CQRD?
2. How much goodput of long bandwidth-greedy flows is sacrificed in CQRD?

## Slide 26: Experiment 1
Single aggregation/core switch (ns2 simulations)
Simulation parameters:
  Link capacity=10Gbps, Link delay=4us, Total buffer size=5MB, TCP initial window size=4, TCP initial RTO=200us.
Traffic:
  1200 TCP flows, Flow size & inter-arrival time from realistic distributions, Random source & destination port
Notes: Our first experiment is to simulate an aggregation or core switch in DCN with huge amount of flows passing by, and compare different approaches in this situation. We simulate a 24 port switch (which is a typical DCN switch) as shown in the figure. During the simulation, 1200 flows derived from realistic distributions are generated to 24 ports. This generates a lot of output-contending and path-contending flows. We evaluate CQRD’s performance under this situation.
All the simulation parameters are listed below.

## Slide 27: Single aggregation/core switch
FCT of all short flows ( < 100KB) and goodput of all large flows (> 100KB) interfered by the giant flows (> 1MB, included by large flows) at moderate load (0.1).
Notes: Due to the time limitation, we only show the FCT of all short flows and goodput of all large flows interfered by the giant flows at moderate load here. Those flows which are not interfered by giant flows perform well and similarly in all the 3 compared approaches, so we omit the results. We also have done more thorough experiments to show how CQRD deals with the interference between output-contending or path-contending flows. More detailed results can be found in the paper.

## Slide 28: Single aggregation/core switch
FCT of all short flows ( < 100KB) and goodput of all large flows (> 100KB) interfered by the giant flows (> 1MB, included by large flows) at moderate load (0.1).
~36% lower
~7% lower
~28% lower
~4% lower
Notes: Let’s look at the figure. We can see that, in CQRD, the average flow completion time of short flows are ~36% lower than HCF, which is the state-of-art end-host transparent solution. Also, the 99 percentile FCT is 28% lower than HCF.
Meanwhile, CQRD only sacrifice less than 8% goodput of those large bandwidth-greedy flows. This shows that CQRD could greatly reduce the FCT of short flows only at the cost of a little goodput of large flows.

## Slide 29: Experiment 2
Multi-stage DCN switching fabric (ns2 simulations)
Simulation parameters:
  Link delay=2us, Agg switch buffer size=5MB, ToR switch buffer size=4MB, TCP initial window size=4, TCP initial RTO=200us.
Traffic:
  2000 TCP flows, realistic distributions; ECMP load-balancing schemes
Notes: Besides a single switch, to understand CQRD’s improvement on flow interference in the multi-layer DCN switch network, then, in the second experiment, we simulate a two layer Spine-leaf DCN. The network consists of 480 end hosts allocated in 24 racks, which are interconnected by 2 aggregation switches and 24 top-of-rack (ToR) switches. During the experiment, 2000 flows are generated randomly among all the hosts. All the other simulation parameters can be found below.

## Slide 30: Single aggregation/core switch
~14% lower
~30% lower
~2.5% lower
~same
FCT of all short flows ( < 100KB) and goodput of all large flows (> 100KB) interfered by the giant flows (> 1MB, included by large flows) at moderate load (0.1).
Notes: We also present the FCT of all short flows and goodput of all large flows interfered by the giant flows at moderate load here. Other results can be found in our paper.
We can see that, using CQRD, FCT of short flows are reduced by 14% and 30% on average and 99 percentile respectively, compared to the state-of-art HCF switch-based approach. However, CQRD only sacrifices a little goodput of long flows.
These two experiments under different situations verify the effectiveness of CQRD.

## Slide 31
Agenda
Background & Motivation
Flow Interference
CQRD Design
Evaluation
Conclusion
Notes: Finally, I make a conclusion to our paper.

## Slide 32: Conclusion
Tackling the root cause of flow interference:
  Need a more fine-grained queue management scheme
  Simple solution: CQRD—switch queue management scheme
  Transparent to end host
  No modification to protocol stack
  Based on underlying techniques available in commodity productions
Reduces the FCT of short flows by 20-44% in a single switch and 8-30% in a multi-stage data center switch network
  At the cost of a minor goodput decrease for large flows
Notes:   First, we analyze the root cause of flow interference and find that it needs a more fine-grained queue management scheme to solve the problem.
  Then, we propose a simple but effective solution, called CQRD. It is totally transparent to end hosts and need no modification to protocol stack. Also, CQRD can be easily implemented using simple and mature techniques which are already available in commodity productions
  Finally, we evaluate the performance of CQRD using thorough simulations. We show that CQRD could reduce the FCT of short flows by 20-44% in a single switch and 8-30% in a multi-stage data center switch network, only at the cost of a minor goodput decrease for large flows.

## Slide 33
Thank You