## Slide 1: Avoiding the Rush Hours: WiFi Energy Management via Traffic Isolation
Justin Manweiler
Romit Roy Choudhury
ACM MobiSys 2011

## Slide 2: WiFi
Time
Zzz…
Zzz…
Between packet bursts, WiFi switches to low-power sleep mode
: Saving Energy through Sleep

## Slide 3: WiFi Sleep Under Contention
Time
Zzz…
Zzz…
Time
Zzz…
Zzz…

## Slide 4: Beacon Wakeups
Bad wakeups =
burst contention
Key intuition: move beacons, spread apart traffic, let clients sleep faster
Traffic
Download

## Slide 5: Measurements
Energy performance on modern WiFi smartphones
Zzz…
Zzz…
vs

## Slide 6: Measuring Power on Nexus One
Simultaneous measurements at 5K hertz

## Slide 7: Energy Profile of Nexus One
With contention:
↑ Idle/Overhear, ↓ Sleep
Deep
Sleep
Beacon
Wakeups
Idle/Overhear
Light Sleep
Transmit/Receive

## Slide 8: Energy Cost of Contention
Chart: Total Energy in Joules (J)
| 1 AP | 2 AP | 3 AP | 4 AP | 5 AP | 6 AP | 7 AP | 8 AP
Iperf | 8.1891 | 10.8792 | 13.2722 | 16.2221 | 20.5357 | 24.4051 | 28.9059 | 35.6658
YouTube | 8.9438 | 9.6042 | 10.4699 | 11.3345 | 12.3492 | 13.5386 | 14.711 | 16.4552
Energy costs grow with number of contenders
Denser Neighborhood
File Download

## Slide 9: Activity Percentages
Chart: File Download
| 1 AP | 2 AP | 3 AP | 4 AP | 5 AP | 6 AP | 7 AP | 8 AP
Deep Sleep | 0.8491 | 0.77659 | 0.71409 | 0.63023 | 0.5133 | 0.41156 | 0.28187 | 0.09757
Light Sleep | 0.031687 | 0.032098 | 0.027745 | 0.030199 | 0.030381 | 0.02225 | 0.027081 | 0.018074
Idle/Overhear | 0.037339 | 0.099094 | 0.16135 | 0.24008 | 0.34846 | 0.45256 | 0.5706 | 0.75405
High Power | 0.081871 | 0.092217 | 0.09681 | 0.099491 | 0.10787 | 0.11363 | 0.12045 | 0.13031
Increasing time in
Idle/Overhear
Transmit/Receive
Time

## Slide 10: SleepWell Design
Avoiding the rush hours to save energy
Seattle 520 bridge
Wakeup later / go home later
Smarter commute = save gas
Smarter beacons = save battery

## Slide 11: SleepWell Techniques
Traffic Monitoring
  APs maintain a map of peers in the wireless vicinity
Traffic Migration
  APs select a new beacon position based on heuristics
Traffic Preemption
  APs avoid traffic spillover into that of neighbors

## Slide 12: Traffic Monitoring
beacon & traffic maps for the one-hop neighborhood

## Slide 13: Traffic Migration
85
25
70
55
0
55
75
50
Expected share =
100/(n + 1) = 25 ms
Claim expected share from largest hole
CONVERGES

## Slide 14: Traffic Preemption
Traffic preemption prevents spillover
25
0
75
50

## Slide 15: Key Implementation Challenge
APs need to change the beacon timings
But, no 802.11 protocol support
Fortunately, clients synchronize to AP clocks
AP can change beacon by “lying” about the time
Fully 802.11 compatible AP:
Hostapd + modified Atheros Ath9k 802.11n driver
40

## Slide 16: Rescheduling Client Wakeups
“hey client
this beacon is
60ms Late”
Actual
Time
Client Clock
(sync to AP)
I’ll adjust
my clock
OK, I need to
wakeup in 40ms
50
50
0
0
Right
on time
I know client will
wakeup in 40ms
Yes, delayed
client by 40ms

## Slide 17: Energy TDMA
Chart: Time (s)
Chart: Time (s)
Chart: Time (s)

## Slide 18: Energy Comparison (8AP)
Chart: Total Energy in Joules (J)
| Iperf | YouTube | Pandora
No Contention | 8.1891 | 8.9438 | 7.7277
802.11, 8 AP | 35.6658 | 16.4552 | 17.6799
SleepWell, 8 AP | 17.3591 | 9.0052 | 10.9639
File Download
802.11
SleepWell

## Slide 19: Activity Percentages: 802.11
Chart: File Download
| 1 AP | 2 AP | 3 AP | 4 AP | 5 AP | 6 AP | 7 AP | 8 AP
Deep Sleep | 0.8491 | 0.77659 | 0.71409 | 0.63023 | 0.5133 | 0.41156 | 0.28187 | 0.09757
Light Sleep | 0.031687 | 0.032098 | 0.027745 | 0.030199 | 0.030381 | 0.02225 | 0.027081 | 0.018074
Idle/Overhear | 0.037339 | 0.099094 | 0.16135 | 0.24008 | 0.34846 | 0.45256 | 0.5706 | 0.75405
High Power | 0.081871 | 0.092217 | 0.09681 | 0.099491 | 0.10787 | 0.11363 | 0.12045 | 0.13031
Transmit/Receive

## Slide 20: Activity Percentages: SleepWell
Chart: File Download
| 1 AP | 2 AP | 3 AP | 4 AP | 5 AP | 6 AP | 7 AP | 8 AP
Deep Sleep | 0.8491 | 0.72442 | 0.63208 | 0.50037 | 0.43769 | 0.34075 | 0.21945 | 0.082568
Light Sleep | 0.031687 | 0.15864 | 0.25221 | 0.3787 | 0.4409 | 0.5393 | 0.63705 | 0.76689
Idle/Overhear | 0.037339 | 0.037719 | 0.037678 | 0.04091 | 0.041459 | 0.04136 | 0.063472 | 0.068927
High Power | 0.081871 | 0.079219 | 0.07803 | 0.080022 | 0.079951 | 0.078584 | 0.08003 | 0.081614
Transmit/Receive

## Slide 21: Youtube CDF, Instantaneous Power
Chart: Power in Milliwatts (mW)
SleepWell closely matches zero-contention energy profile
8AP,
SleepWell
8AP, 802.11

## Slide 22: Throughput under SleepWell (per-link TCP on 4 AP testbed)
Chart: throughput(Mbps)
Negligible performance impact:
SleepWell just reorders traffic

## Slide 23: Limitations
Not immediately suitable to interactive traffic (VoIP)
  True of 802.11 PSM in general
Legacy APs lessen energy savings
  Won’t preempt for SleepWell traffic
Contention from clients of the same AP
  Considered in NAPman [MobiSys 2010]

## Slide 24: Prior Work
WiFi PSM Sleep Optimization
  NAPman, Catnap [MobiSys 10]
  μPM [MobiSys 08]
WiFi Duty Cycling
  Wake-on-Wireless [MobiCom 02] / revisited [MobiSys 07]
  Context-for-Wireless [MobiSys 07]
  Blue-Fi [MobiSys 09], Breadcrumbs [MobiCom 08]
  Also, Turducken, Coolspots, Tailender, etc.
Sensor network TDMA
  Z-MAC [SenSys 05]
  S-MAC [INFOCOM 02]

## Slide 25: Conclusion
PSM is a valuable energy-saving optimization
But, PSM designed with a single AP in mind
Multiple APs induce contention, waste energy
Staggered wakeups  clients sleep through contention
SleepWell = PSM made efficient for high-density networks
Zzz…
Zzz…
to

## Slide 26: Thank you!
Questions?
cs.duke.edu/~jgm
jgm@cs.duke.edu