## Slide 1
Rahul Potharaju (Purdue University)
Navendu Jain (Microsoft Research)
October 23-25, 2013
IMC 2013
Demystifying the Dark Side of the Middle
A Field Study of Middlebox Failures in Datacenters

## Slide 2: Middlebox reliability – Where do we stand today?
Chart: 
| L2 Switches | L3 Routers | Middleboxes | Others
High Severity Incidents | 20 | 36 | 43 | 1
Population | 81 | 2 | 11 | 3
Source: High-Severity Incidents 2008-12
Contribute to 43% of high severity incidents despite being 11% of the population
AIM: Understand middlebox failures to improve service reliability

## Slide 3: Inside a Datacenter
INTERNET
Servers
Top of Rack (ToR) switch
Aggregation switch
Access routers/
Core fabric
1:1 network redundancy
Note: Other configurations are possible e.g., firewalls at the network edge.
IDPS
VPN
FIREWALL
LOAD
BALANCER
IDPS
VPN
FIREWALL
LOAD
BALANCER

## Slide 4: Aim: Data driven approach to improve middlebox reliability
Q1: Middlebox Failure Characteristics
How reliable are middleboxes?
How often do they fail and for how long?
Q2: Failure Root Causes
What causes middlebox failures?
What are the main resolution actions?
Q3: Middlebox Redundancy
Is middlebox redundancy 100% effective in masking failures?
?
?
Redundancy Group

## Slide 5: Extracting Impactful Failures
2
CHALLENGE:
How to measure failure impact?
1
CHALLENGE:
How to remove duplicate events?
SYSLOG/SNMP Events
(July 2010-2012)
3
CHALLENGE:
How to determine problem root cause?
Impactful Failures + Problem Root Causes
1.96M raw events
5
?
Errr… did a service get impacted?
What caused the failure?
Switch A
Switch B
Switch C
T1: Switch B is down
T2: Switch B is down
T3: ……………………….
T1: Switch B is down
T2: Switch B is up
T3: Switch B is down
?
NOISY/REDUNDANT MESSAGES
Link Down
Firewall
Switch
TIME
Event A
Event B
Overlapping Events
Pick earliest
end time
Event A
Event B
Pick earliest
start and
end time
How to define a middlebox failure?
Faulty load balancers cause throughput loss
Misconfigured firewalls incorrectly forward traffic
Failure Impact?
Time-based Grouping
Traffic Impact
Functional Impact

## Slide 6: How to measure traffic impact?
LINK DOWN
Time
Traffic flowing on a link
Traffic before the failure
Traffic during the failure
KEY CHALLENGE-1
How do you compare the traffic distributions before and during the failure?
KEY CHALLENGE-2
What time window to pick to compute the traffic distributions?
Option 1: Small time window
(e.g., 5 minutes, 10 minutes)
Problem: May be susceptible to bursty traffic
Option 2: Large time window
(e.g., time of day, daily, weekly)
Problem: May be susceptible to time of day effects and assumes long-term predictability of traffic
Smaller Time Window
Larger Time Window

## Slide 7: Traffic Impact: Use Mann-Whitney-Wilcoxon Test
LINK DOWN
Time
Traffic flowing on a link
Traffic before the failure
Traffic during the failure
KEY CHALLENGE-1
How do you compare the traffic distributions before and during the failure?
KEY CHALLENGE-2
What time window to pick to compute the traffic distributions?
KEY CHALLENGE-2
What time window to pick to compute the traffic distributions?
KEY CHALLENGE-1
How do you compare the traffic distributions before and during the failure?
Parameterize the time window size and compute the accuracy

## Slide 8: Traffic Impact: Use Mann-Whitney-Wilcoxon Test
Time window | % where p-value < 0.05
8 hours | 82.2%
6 hours | 91.1%
4 hours | 92.2%
2 hours | 99.3%
1.5 hours | 91.8%
1 hour | 88.7%
Time window
% where p
-
value < 0.05
8 hours
82.2%
6 hours
91.1%
4 hours
92.2%
2 hours
99.3%
1.5 hours
91.8%
1 hour
88.7%
Null Hypothesis: Traffic values observed before a failure and during a failure follow the same distribution

## Slide 9: Extracting Impactful Failures
2
CHALLENGE:
How to measure failure impact?
1
CHALLENGE:
How to remove duplicate events?
SYSLOG/SNMP Events
(July 2010-2012)
3
CHALLENGE:
How to determine problem root cause?
Impactful Failures + Problem Root Causes
1.96M raw events
Link Down
Firewall
Switch
Time-based Grouping
Traffic Impact
Functional Impact
2
CHALLENGE:
How to measure failure impact?
1
CHALLENGE:
How to remove duplicate events?
SYSLOG/SNMP Events
(July 2010-2013)
3
CHALLENGE:
How to determine problem root cause?
Impactful Failures + Problem Root Causes
1.96M raw events
9
Link Down
Firewall
Switch
How to define a middlebox failure?
Faulty load balancers cause throughput loss
Misconfigured firewalls incorrectly forward traffic
69K
NETSIEVE
(NSDI’13)

## Slide 10
Q1: Middlebox Failure Characteristics
How reliable are middleboxes?
How often do middleboxes fail and for how long?

## Slide 11: How reliable are middleboxes?
VPNs and Firewalls exhibited similar 95P values of 5-7 annual failures per device
Exhibit the highest 95P value of 8.3 failures per device per year
Exhibit the lowest 95P value of 3 failures per device per year
Chart: COV
| LB-1 | LB-2 | LB-3
COV | 5.8 | 0.8 | 1.3
LB-1 and LB-3 – “few bad apples effect”
Faulty power supply units were replaced in isolation over two years
Memory errors masked by the quick-fix solution of reboots
Firewalls exhibited a long tail of up to 24 failures per device per year

## Slide 12: How often do middleboxes fail?
Failure prone devices exhibiting numerous failures within 10s of minutes to a few hours
Robust devices that fail at most once in one or two months
Time between failures (seconds) – log scale

## Slide 13: How long do middleboxes fail?
Short-lived transient failures lasting a few minutes
Long-term failures lasting ≈ 1-10 days – hardware replacements or complex software problems
Time to repair (seconds) – log scale

## Slide 14: Takeaways: Middlebox Failure Characteristics
Most failures are short-lived
  Grey failures (connectivity errors, link flaps) lasting a few minutes to a few hours
  Long-term failures (hardware faults, software problems) lasting 1-10 days
Median number of annual failures is small (1-3), but there is a long tail
  IDPS exhibit highest annual failures per device (95P value of 8.3) while LBs exhibit lowest (95P value of 3)
Presence of the few bad apples effect
  COV >1 for LB-1 and LB-3
  Firewalls have a relatively long tail of up to 24 annual failures per device

## Slide 15
Q2: Failure Root Causes
What causes middlebox failures?
What are the main resolution actions?

## Slide 16: What causes failures?
Chart: 
| Connectivity Errors | Hardware | Misconfigurations | Overload | Software
Firewall | 39 | 25 | 12 | 19 | 5
IDPS | 55 | 28 | 4 | 7 | 4
Load Balancer | 57 | 19 | 13 | 4 | 7
VPN | 78 | 1 | 15 | 4 | 1
Fraction of tickets (%)
Device/neighbor unreachable, link flaps, ARP conflicts, address, parity errors, checksum failed
Faulty power supply units, memory errors, defective chassis/disks/line cards
Bad rules, VLAN misallocation, configuration conflict, mismatched crypto keys
High utilization and firmware bugs
Grey failures (connection errors/interface problems) are dominant
Hardware faults, misconfigurations and overload problems occur, but they are not in majority

## Slide 17: What are the main resolution actions?
Chart: 
| Cable | Reboot | Device | Component | Software
Firewall | 24 | 20 | 0 | 56 | 0
IDPS | 21 | 33 | 0 | 45 | 0
LB | 27 | 26 | 11 | 36 | 0
VPN | 21 | 21 | 0 | 52 | 7
Fraction of tickets (%)
Component replacements was a majority fix
Chart: 
| Disk | PSU | Line Card | Fan | Chassis | Supervisor
Firewall | 20 | 16 | 12 | 0 | 8 | 0
IDPS | 29 | 8 | 0 | 4 | 4 | 0
LB | 22 | 8 | 0 | 0 | 6 | 0
VPN | 31 | 0 | 14 | 0 | 0 | 7
Disks and power supply units were among the most defective hardware components
Low cost solutions (cable cleaning/replacements, reboot) are typically explored first to mitigate service downtime
Software was relatively more stable for middleboxes

## Slide 18: Summary: Root Cause Analysis
Grey failures are dominant:
  Implication: Develop robust network protocols (e.g., multi-path TCP) to route traffic around interfaces exhibiting intermittent connectivity
Wide variety of misconfigurations present:
  Implication: Develop Software-defined networks (SDN) based configuration management tools
Hardware faults, misconfigurations and overload problems are present; not in majority
Cable replacement and reboots are the most popular quick-fix solutions to mitigate middlebox problems

## Slide 19
Q3: Middlebox Redundancy
Is middlebox redundancy 100% effective in masking failures?

## Slide 20: How to evaluate effectiveness of middlebox redundancy?
Redundancy group
ACTIVE
STANDBY
ACTIVE
STANDBY
Aggregation
Switches
Load
Balancers
IDEA: Compare median traffic before and during the failure across all links in the redundancy group
Redundancy is
100% effective

## Slide 21: How effective is middlebox redundancy?
Other Middleboxes | 
Middlebox Type | % cases where redundancy group experienced simultaneous failure
Firewalls | 33%
IDPS | 1%
VPNs | 0%
Chart: 
| LB-AGG
Individual | 0.55
Group | 0.92
Network Layer
Median Normalized traffic
Individual failures have the most impact
… but redundancy nearly masks these failures
improving the median traffic carried by 67%
Y = 1  No traffic loss
What causes an unsuccessful redundancy failover? | 
Faulty failovers | Protocol bugs Bad cables Software version incompatibilities
Misconfigurations | Copy/paste errors Mismatched cryptographic keys Expired certificates

## Slide 22: Conclusion
Goal: Data-driven approach to improve middlebox reliability
Key Findings:
  Grey failures (e.g., connectivity errors, interface flaps) dominate middleboxes
  Hardware faults, misconfigurations and overload problems are present but they are not in the majority
  Variety of misconﬁgurations such as incorrect rules, VLAN misallocation and mismatched cryptographic keys
  Middlebox redundancy is ineffective in 33% of the cases for Firewalls and Load balancers; nearly 100% effective for IDPS and VPNs
  Some types of middleboxes exhibit the few bad apples effect

## Slide 23: Thank You
http://research.microsoft.com/projects/netwiser/