## Slide 1
Rahul Potharaju (Purdue University)
Navendu Jain (Microsoft Research)
October 1-3, 2013
SoCC 2013

## Slide 2: Service Reliability – Where do we stand today?

## Slide 3: How do network failures impact services?
Chart: 
| SLA Violation | Service Errors | Security Issues | High latency/Packets Drops | Connectivity Loss
Inter-DC | 12 | 43 | 2 | 15 | 29
Intra-DC | 6 | 16 | 2 | 7 | 70
Latency, content rendering and timeouts for CDN services
Authentication issues
High latency from web to db tiers; parity errors on switches
Failures causing service impact (%)
Type of Service Impact
Replication problems due to stale data; timeouts when uploading files
Dropped connections; loss of application packets
* Data source: High-severity incidents (2008-13)

## Slide 4: Inside a Datacenter
INTERNET
Servers
Top of Rack (ToR) switch
Aggregation switch
Access routers/
Core fabric
1:1 network redundancy
Long-haul fiber links

## Slide 5: Aim: Data driven approach to improve service reliability
Q1: Network domain availability
How many independent network domains do we need to deliver 99.99% availability?
?
?
Q2: Network failures
What are their root causes?
Q3: Failure Analysis
How effective are repairs in fixing failures?
Q4: Capacity vs. Availability
How reliable are expensive scale-up switches vs. commodity scale-out ones?
NETWORK DOMAIN
Access routers
Aggregation switches
Top-of-Rack switches

## Slide 6: Extracting Impactful Failures
2
CHALLENGE:
How to measure failure impact?
59.8K
1
CHALLENGE:
How to remove duplicate events?
SYSLOG/SNMP Events
(July 2010-2013)
3
CHALLENGE:
How to determine problem root cause?
Impactful Failures + Problem Root Causes
23M raw events
6
Traffic Level Impact
Network
Traffic Data
Network
Trouble Tickets
Time-based Grouping
Service Level Impact
?
Errr… did a service get impacted?
What caused the failure?
Switch A
Switch B
Switch C
T1: Switch B is down
T2: Switch B is down
T3: ……………………….
T1: Switch B is down
T2: Switch B is up
T3: Switch B is down
?
NOISY/REDUNDANT MESSAGES
Link Down
Switch A
Switch B
TIME
A
B
Overlapping Events
Pick earliest
end time
A
B
Pick earliest
start and
end time

## Slide 7
Q1: Network domain availability
How effective is network redundancy?
How many independent network domains are needed to deliver an uptime SLA of 99.99%?
NETWORK DOMAIN

## Slide 8: How to evaluate effectiveness of network redundancy?
ACTIVE
STANDBY
ACTIVE
STANDBY
Access routers
Aggregation switches
Redundancy group
X
Redundancy is
100% effective
IDEA: Compare median traffic before and during the failure across all links in the redundancy group

## Slide 9: How effective is network redundancy?
Chart: 
| AGG-ToR | ACCR-AGG | CORE-ACCR | CORE-CORE | ALL
Individual | 0.73 | 0.82 | 0.79 | 0.89 | 0.76
Group | 0.94 | 0.87 | 0.98 | 1 | 0.92
Network Layer
Median Normalized traffic
AGG-ToR link failures have the most impact
Inter-datacenter link failures are completely masked
Redundancy least effective at the AR–AGG layer
Network redundancy reduces traffic loss by 21%
… but redundancy nearly masks these failures
Y = 1  No traffic loss

## Slide 10: How many independent network domains to meet uptime SLA?
Number of domains for SLA = 99.9%
(maximum 8.76 hours of downtime per year)
Chart: 
| ALL
Individual | 0.76
Group | 0.92
Median Normalized traffic
Solve for the minimum integer n
Number of domains for SLA = 99.99%
(maximum 52 minutes of downtime per year)

## Slide 11
Q2: Failure Root Causes
Are hardware faults dominant?
How frequent are software bugs?
Are humans making mistakes?
?
?

## Slide 12: What causes intra-DC network failures?
Chart: 
| Interface Errors | Device Failures | Network Card Failures | Memory Errors | OS bugs | Unexpected reloads | Misconfigurations
Access router | 76.4 | 55.5 | 17.4 | 14.5 | 0.3 | 7.2 | 8.4
Aggregation switch | 78.2 | 14.3 | 26.2 | 8.5 | 0.2 | 24 | 0
Top-of-Rack switch | 64.3 | 8.4 | 12.6 | 7.2 | 7.2 | 22.1 | 7.1
Fraction of tickets (%)
Faulty cables/optical transceivers, protocol convergence delays
Hardware failures are significant
Incorrect routes, connecting the wrong neighbor

## Slide 13: What causes inter-DC failures?
Chart: 
| Link Flapping | High Link Utilization | Unplanned Change | Line Card Failures | Fiber Cuts | Misconfigurations | Software Errors
Series 1 | 36.12 | 29.9 | 6.2 | 5.9 | 5.8 | 3.1 | 2.2
Recent efforts to increase WAN utilization:
Software-driven WANs: Hong et al. (Sigcomm 2013)
B4: Jain et al. (Sigcomm 2013)
NetStitcher: Laoutaris et al. (Sigcomm 2011)
Fraction of tickets (%)
High number of packet errors or discards. Route re-convergence takes 2x-3x longer than expected
Physical layer problem (e.g., fiber cuts) triggers an optical re-route

## Slide 14
Q3: Failure analysis
How effective are repairs in fixing failures?
?
?

## Slide 15: Are repairs effective?
Chart: 
| Access router | Aggregation switch | Top-of-Rack switch
P[1st Failure] | 0.25 | 0.17544 | 0.05848
P[2nd ¦ 1st] | 0.19231 | 0.16393 | 0.12987
P[3rd ¦ 2nd] | 0.17241 | 0.11628 | 0.18519
Probability of failure
Exhibit a decreasing trend to fail after each repair
Increasing trend – Repairs are not quite effective
Likely reasons
ToRs are low-priority devices; quick-fix solutions (e.g., reboot) risks delaying finding the true root cause
Probability(1st failure)
Probability(2nd failure | 1st Failure)
Probability(3rd failure | 2nd failure)

## Slide 16
Q4: Capacity vs. Availability
How reliable are expensive scale-up switches vs. commodity scale-out ones?

## Slide 17: Scale-up vs. Scale-out
 |  | Switch-A (Scale-up) | Switch-B (Scale-out) |  | 
 | Capacity | High | Low | Capacity | 
 | Cost ($/port) | High | Low | Cost ($/port) | 
 | Management | Easy | Hard | Management | 
 | Reliability | ?? | ?? | Reliability | 

## Slide 18: Distribution of ToR counts across AGGs
Category 1 (Low TOR Count)
Category 2
Category 3
Category 4 (High TOR Count)
2
Categorize the AGGs based on quantiles
3
Compute AGG availability based on the number of logged failures
Aggregation switch
Top-of-Rack switch
1
Compute the distribution of #ToRs connected to AGGs
18
Port count utilization < 50%
High median availability (~ 99.99%)
Scale-out switches deliver relatively higher availability
Port count utilization > 50%
Low median availability (~ 99.9%)

## Slide 19: Conclusion
Goal: Data-driven approach to improve service reliability
[Q1]: How many independent network domains do we need to meet an uptime SLA?
  Build multiple small network domains: 3 for 99.9% availability; 4 for 99.99% availability
[Q2]: What causes network failures?
  Intra-DC problem causes: Interface errors, hardware failures, and unexpected reboots
  Inter-DC problem causes: Link flapping, high link utilization, and unplanned changes
[Q3]: Are repairs effective in fixing device failures?
  Repairs are relatively more effective for ARs and AGGs; not for ToRs
[Q4]: How reliable are expensive scale-up switches vs. commodity scale-out ones?
  Scale-out switches deliver relatively higher availability
Future Work: Study the overall impact of redundancy mechanisms at storage, compute, and network layers

## Slide 20: Thank You
http://research.microsoft.com/projects/netwiser/