## Slide 1
Video Streaming on the Internet
Computer Networking: A Top Down Approach 6th edition Jim Kurose, Keith Ross Addison-Wesley
Adopted from JFK/KWR’s Slides
All material copyright 1996-2012
J.F Kurose and K.W. Ross, All Rights Reserved
Notes: A very brief version, slide 8, 9, 56…

## Slide 2: What’s the Internet: “nuts and bolts” view
millions of connected computing devices:
  hosts = end systems
  running network apps
communication links
  fiber, copper, radio, satellite
  transmission rate: bandwidth
Packet switches: forward packets (chunks of data)
  routers and switches
wired
links
wireless
links
router
mobile network
global ISP
regional ISP
home
network
institutional
network
smartphone
PC
server
wireless
laptop
Notes: 2

## Slide 3: What’s the Internet: a service view
Infrastructure that provides services to applications:
  Web, VoIP, email, games, e-commerce, social nets, …
provides programming interface to apps
  hooks that allow sending and receiving app programs to “connect” to Internet
  provides service options, analogous to postal service
mobile network
global ISP
regional ISP
home
network
institutional
network

## Slide 5: Quality of Experience (QoE) today is not ideal

## Slide 6
https://gigaom.com/2012/11/09/online-viewers-start-leaving-if-video-doesnt-play-in-2-seconds-says-study/
Video: La Luna (Pixar 2011)
Users start leaving if video doesn’t play in 2 seconds
Notes: When we stream a video from the internet, we all have this annoying experience -- the video suddenly gets stuck and starts rebuffering ..
Studies actually show that users start leaving if the video doesn’t play in 2 seconds.
And given that fact that video streaming has been dominating today's internet traffic, this kind of bad experience will lead to tremendous loss of users. Therefore industry and academia have devoted lots efforts to improve video streaming experience.

## Slide 7: Multimedia: video
video: sequence of images displayed at constant rate
  e.g. 24 images/sec
digital image: array of pixels
  each pixel represented by bits
coding: use redundancy within and between images to decrease # bits used to encode image
  spatial (within image)
  temporal (from one image to next)
……………………...…
spatial coding example: instead of sending N values of same color (all purple), send only two values: color value (purple) and number of repeated values (N)
……………………...…
frame i
frame i+1
temporal coding example: instead of sending complete frame at i+1, send only differences from frame i

## Slide 8: Streaming stored video:
video
recorded (e.g., 30 frames/sec)
2. video
sent
Cumulative data
streaming: at this time, client
playing out early part of video,
while server still sending later
part of video
network delay
(fixed in this example)
time
3. video received,
played out at client
(30 frames/sec)

## Slide 9: Streaming stored video: challenges
continuous playout constraint: once client playout begins, playback must match original timing
  … but network delays are variable (jitter), so will need client-side buffer to match playout requirements
  video packets may be lost, retransmitted

## Slide 10: Web and HTTP
First, a review…
web page consists of objects
object can be HTML file, JPEG image, Java applet, audio file,…
web page consists of base HTML-file which includes several referenced objects
each object is addressable by a URL, e.g.,
www.someschool.edu/someDept/pic.gif
host name
path name

## Slide 11: HTTP overview
HTTP: hypertext transfer protocol
Web’s application layer protocol
client/server model
  client: browser that requests, receives, (using HTTP protocol) and “displays” Web objects
  server: Web server sends (using HTTP protocol) objects in response to requests
PC running
Firefox browser
server
running
Apache Web
server
iphone running
Safari browser
HTTP request
HTTP response
HTTP request
HTTP response
Notes: [uh-pach-ee]

## Slide 12: Adaptive Multi-Bit Rate with HTTP Streaming （1）
Client-centric architecture with stateful client and stateless server
  Standard server: Web servers
  Standard Protocol: HTTP
  Session state and logic maintained at client
Video is broken into multiple chunks
Chunks begin with keyframe so independent of other chunks
A series of HTTP progressive downloads of chunks
Playing chunks in sequence gives seamless video

## Slide 13: Adaptive Multi-Bit Rate with HTTP Streaming （2）
Encode video at different levels of quality/bandwidth
Client can adapt to different bit rates within a single session by requesting different sized chunks
Chunks of different bit rates must be synchronized
  All encodings have the same chunk boundaries and all chunks start with key frames, so you can make smooth splices to chunks of higher or lower bit rates

## Slide 14: HTTP Chunking Protocol
HTTP Adaptive Player
Web browser
Web server
HTTP
TCP
…
HTTP
TCP
…
A1
A1
A2
B1
B2
A1
B1
Cache
Client
Web server
…
…
A1
A2
B1
B2
HTTP GET A1
Server
B2
HTTP GET B2